Project Carbon — JC Series Bus
	Description	Pin	B	A	Pin	Description
JC-40 (Standard)	+5 V DC power	+5V	B1	A1	GND	Ground	JC-40 (Standard)
	Machine cycle 1 indicator	/M1	B2	A2	/RESET	Primary reset
	Interrupt request	/INT	B3	A3	CLK	Primary clock
	Memory request	/MREQ	B4	A4	A0	16-bit address bus
	I/O request	/IORQ	B5	A5	A1
	Write strobe	/WR	B6	A6	A2
	Read strobe	/RD	B7	A7	A3
	−12 V DC power	−12V	B8	A8	A4
	Serial transmit	TX	B9	A9	A5
	Serial receive	RX	B10	A10	A6
	+12 V DC power	+12V	B11	A11	A7
	8-bit data bus	D0	B12	A12	A8
		D1	B13	A13	A9
		D2	B14	A14	A10
		D3	B15	A15	A11
		D4	B16	A16	A12
		D5	B17	A17	A13
		D6	B18	A18	A14
		D7	B19	A19	A15
	+5 V DC power	+5V	B20	A20	GND	Ground
JC-64 (Enhanced)	+12 V DC power	+12V	B21	A21	GND	Ground	JC-64 (Enhanced)
	+3.3 V DC power	+3.3V	B22	A22	GND	Ground
	Secondary serial transmit	TX2	B23	A23	A16	24-bit address bus
	Secondary serial receive	RX2	B24	A24	A17
	Non‑maskable interrupt	/NMI	B25	A25	A18
	CPU wait request	/WAIT	B26	A26	A19
	CPU halt indicator	/HALT	B27	A27	A20
	Bus request	/BUSREQ	B28	A28	A21
	Bus acknowledge	/BUSACK	B29	A29	A22
	Secondary clock	CLK2	B30	A30	A23
	Secondary reset	/RESET2	B31	A31	/RFSH	Refresh cycle indicator
	+5 V DC power	+5V	B32	A32	GND	Ground
JC-80 (Advanced)	Trap breakpoint	/TRAP	B33	A33	GND	Ground	JC-80 (Advanced)
	Address latch enable	ALE	B34	A34	GND	Ground
	Zilog direct memory access	/BAI	B35	A35	IEI	Zilog interrupt requests
		/BAO	B36	A36	IEO
	Direct memory access	/DREQ0	B37	A37	/IRQ0	Interrupt requests
		/DACK0	B38	A38	/IRQ1
		/DREQ1	B39	A39	/IRQ2
		/DACK1	B40	A40	/IRQ3
JC-100 (Ultimate)	Direct memory access	/DREQ2	B41	A41	/IRQ4	Interrupt requests	JC-100 (Ultimate)
		/DACK2	B42	A42	/IRQ5
		/DREQ3	B43	A43	/IRQ6
		/DACK3	B44	A44	/IRQ7
	(Unassigned)	(NC)	B45	A45	(NC)	(Unassigned)
	(Unassigned)	(NC)	B46	A46	(NC)	(Unassigned)
	Bus lock	/LOCK	B47	A47	VMA	Valid memory address
	Program store enable	/PSEN	B48	A48	/FIRQ	Fast interrupt request
	+12 V DC power	+12V	B49	A49	GND	Ground
	+5 V DC power	+5V	B50	A50	GND	Ground
JC-120 (eXtended)	16-bit data bus	D8	B51	A51	/BHE	Byte high enable	JC-120 (eXtended)
		D9	B52	A52	(RES)	(Reserved)
		D10	B53	A53	(NC)	(Unassigned)
		D11	B54	A54	(NC)	(Unassigned)
		D12	B55	A55	(NC)	(Unassigned)
		D13	B56	A56	(NC)	(Unassigned)
		D14	B57	A57	(NC)	(Unassigned)
		D15	B58	A58	(NC)	(Unassigned)
	+3.3 V DC power	+3.3V	B59	A59	GND	Ground
	+5 V DC power	+5V	B60	A60	GND	Ground